## Slide 1: Arduino Workshop #7
Shift Registers
Notes: 24 – Arduino Uno
24 – USB cable
192 – Red LED
72 – Yellow LED
120 – Green LED
192 – 220 Ω resistors
24 – SN74HC595N shift register DIP IC
24 – Sharp GP2Y0A41SK0F IR distance sensor (with cable)
24 – Jumper Wire Sets
24 – Breadboards

## Slide 2: Looking at the 74HC595 Shift register pin-out diagram
Pins QB to QH
  The eight parallel outputs of the shift register
VCC
  Connect to 5 V
GND
  Shared ground with the arduino
SER
  Where we will feed 8 sequential bits to set the value of the parallel out puts
SRCLK
  Clock pin
    Every time this is high the value shifts by 1 bit
    8 pulses will pull all the data we are sending
RCLK
  Latch pin (register clock pin)
    Allows to sequentially shift data

## Slide 3: How it works

## Slide 4: Let's look at the new Arduino code
Conveniently, Arduino has a built in shift function
shiftOut()
It accepts 4 parameters
Data pin number
Clock pin number
Bit order
The value to shift out
If for example you want to shift out the alternating pattern shown previously you would write
shiftOut(DATA, CLOCK,MSBFIRST, B10101010);
Data and clock are set to the pin number for those lines
MSBFIRST indicates the most significant bit (leftmost) is sent first
B in the last parameter tells the Arduino IDE to interpret as binary rather than a decimal

## Slide 5: Lets wire up what we just looked at
Data is pin 8
Latch is pin 9
Clock is pin 10
Don't forget the current limiting resistors for the LEDS

## Slide 6: Writing the code
Because the shift registry will latch the values, you only need to send them one time in the setup
This program follows the flow chart shown earlier
Latch pin is set low
8 bits of data shifted in (using shiftOut())
Latch pin is set high

## Slide 7: Animation using shift register
We can make a light rider (leds chase each other back and forth) with the same circuit as before
We will simply change how we implement shiftOut()
Because shiftout() is very fast we can update the register thousands of times per second
We just need to know the binary code we want the leds to follow (and then we need to convert that into a decimal)
  Store that as a sequence
  Iterate the sequence and use the value as the shift value
    For loop works good here

## Slide 8: Code to make this happen
Change things up
Speed the lights up or down
  Change the delay
Make a different pattern
  Change the values in the sequence -- remember they are a decimal conversion from binary value

## Slide 9: LED bar graph

## Slide 10: Use our knowledge
Goal:
Make the LED lights respond as a bar graph to how close your hand (or other object is)
Using our knowledge of analog sensors and the shift registry
Using a IR distance sensor to change the registry
We are also going to need to map the receiver values (0 to 500) to 4 bits (0 to 8) range

## Slide 11: Wire it up

## Slide 12: What we want as the result
Where each line is some distance away from the receiver and as we get closer to the receiver more lights light up
Try this first, we will look at one possible solution in a moment
Note the values next to each line is the decimal conversion of the binary shown

## Slide 13: One code solution